## Slide 1
Computer Networking: A Top-Down Approach 8th edition Jim Kurose, Keith Ross Pearson, 2020
Chapter 6 The Link Layer
and LANs
A note on the use of these PowerPoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
For a revision history, see the slide note for this page.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2020
J.F Kurose and K.W. Ross, All Rights Reserved
Notes: Version History
8.0 (May 2020)
All slides reformatted for 16:9 aspect ratio
All slides updated to 8th edition material
Use of Calibri font, rather that Gill Sans MT
Add LOTS more animation throughout
lighter header font
Updated datacenter slides, day-in-the-life

## Slide 2: Link layer and LANs: our goals
understand principles behind link layer services:
  error detection, correction
  sharing a broadcast channel: multiple access
  link layer addressing
  local area networks:
  Ethernet
instantiation, implementation of various link layer technologies

## Slide 3: Link layer, LANs: roadmap
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches

## Slide 4: Link layer: introduction
terminology:
hosts and routers: nodes
communication channels that connect adjacent nodes along communication path: links
  wired
  wireless
  LANs
layer-2 packet: frame, encapsulates datagram
mobile network
enterprise
network
national or global ISP
datacenter
network
link layer has responsibility of
transferring datagram from one node
to physically adjacent node over a link

## Slide 5: Link layer: context
datagram transferred by different link protocols over different links:
  e.g., WiFi on first link, Ethernet on next link
each link protocol provides different services
  e.g., may or may not provide reliable data transfer over link
transportation analogy:
trip from Princeton to Lausanne
  limo: Princeton to JFK
  plane: JFK to Geneva
  train: Geneva to Lausanne
tourist = datagram
transport segment = communication link
transportation mode = link-layer protocol
travel agent = routing algorithm

## Slide 6: Link layer: services
framing, link access:
  encapsulate datagram into frame, adding header, trailer
  channel access if shared medium
  “MAC” addresses in frame headers identify source, destination (different from IP address!)
reliable delivery between adjacent nodes
  we already know how to do this!
  seldom used on low bit-error links
  wireless links: high error rates
    Q: why both link-level and end-end reliability?
…
…

## Slide 7: Link layer: services (more)
flow control:
  pacing between adjacent sending and receiving nodes
error detection:
  errors caused by signal attenuation, noise.
  receiver detects errors, signals retransmission, or drops frame
error correction:
  receiver identifies and corrects bit error(s) without retransmission
half-duplex and full-duplex:
  with half duplex, nodes at both ends of link can transmit, but not at same time
…
…

## Slide 8: Where is the link layer implemented?
in each-and-every host
link layer implemented in network interface card (NIC) or on a chip
  Ethernet, WiFi card or chip
  implements link, physical layer
attaches into host’s system buses
combination of hardware, software, firmware
controller
physical
cpu
memory
host bus
(e.g., PCI)
network interface
application
transport
network
link
link
physical

## Slide 9: Interfaces communicating
controller
physical
memory
CPU
controller
physical
cpu
memory
application
transport
network
link
link
physical
application
transport
network
link
link
physical
sending side:
encapsulates datagram in frame
adds error checking bits, reliable data transfer, flow control, etc.
receiving side:
looks for errors, reliable data transfer, flow control, etc.
extracts datagram, passes to upper layer at receiving side
linkh
linkh
datagram
datagram
datagram

## Slide 10: Link layer, LANs: roadmap
a day in the life of a web request
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
  VLANs
link virtualization: MPLS
data center networking

## Slide 11: Error detection
EDC: error detection and correction bits (e.g., redundancy)
D: data protected by error checking, may include header fields
Error detection not 100% reliable!
  protocol may miss some errors, but rarely
  larger EDC field yields better detection and correction
datagram
D
EDC
d data bits
bit-error prone link
D’
EDC’
all
bits in D’
OK
?
N
detected
error
otherwise
datagram

## Slide 12: Parity checking
single bit parity:
detect single bit errors
0111000110101011
1
parity
bit
d data bits
two-dimensional bit parity:
detect and correct single bit errors
d1,1
d2,1
di,1
. . .
d1,j+1
d2,j+1
di,j+1
. . .
. . .
d1,j
d2,j
di,j
. . .
di+1,1
di+1,j+1
di+1,j
. . .
. . .
. . .
. . .
row parity
column
parity
0 1 1 1 0 1
1 0 1 0 1 1
1 1 1 1 0 0
1 0 1 0 1 0
no errors:
0 1 1 1 0 1
1 0 1 0 1 1
1 0 1 1 0 0
1 0 1 0 1 0
parity
error
parity
error
detected
and
correctable
single-bit
error:
Even parity: set parity bit so there is an even number of 1’s
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 13: Internet checksum (review)
sender:
treat contents of UDP segment (including UDP header fields and IP addresses) as sequence of 16-bit integers
checksum: addition (one’s complement sum) of segment content
checksum value put into UDP checksum field
receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  not equal - error detected
  equal - no error detected. But maybe errors nonetheless? More later ….
Goal: detect errors (i.e., flipped bits) in transmitted segment

## Slide 14: Cyclic Redundancy Check (CRC)
more powerful error-detection coding
D: data bits (given, think of these as a binary number)
G: bit pattern (generator), of r+1 bits (given)
goal: choose r CRC bits, R, such that <D,R> exactly divisible by G (mod 2)
  receiver knows G, divides <D,R> by G. If non-zero remainder: error detected!
  can detect all burst errors less than r+1 bits
  widely used in practice (Ethernet, 802.11 WiFi)
r CRC bits
d data bits
D
R
<D,R> = D 2r XOR R
*
bit pattern
formula for bit pattern

## Slide 15: Cyclic Redundancy Check (CRC): example
We want:
  D.2r XOR R = nG
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
D.2r
G
R = remainder [ ]
or equivalently:
  D.2r = nG XOR R
or equivalently:
if we divide D.2r by G, want remainder R to satisfy:
1 0 0 1
1 0 1 0
1 0 1
0 0 0
1 0 0 1
1 0 0 1
1 0 0 1
0 0 0
1 1 0
1 1 0 0
1 0 1 0
0 1 1
0 1 1
D
R
1 0 0 1
G
0 0 0
1 0 1 1 1 0
2r
*
1
0
1

## Slide 16: Link layer, LANs: roadmap
a day in the life of a web request
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
  VLANs
link virtualization: MPLS
data center networking

## Slide 17: Multiple access links, protocols
two types of “links”:
point-to-point
  point-to-point link between Ethernet switch, host
  PPP for dial-up access
broadcast (shared wire or medium)
  old-fashioned Ethernet
  upstream HFC in cable-based access network
  802.11 wireless LAN, 4G/4G. satellite
shared wire (e.g.,
cabled Ethernet)
shared radio: WiFi
shared radio: satellite
humans at a cocktail party
(shared air, acoustical)
shared radio: 4G/5G

## Slide 18: Multiple access protocols
single shared broadcast channel
two or more simultaneous transmissions by nodes: interference
  collision if node receives two or more signals at the same time
distributed algorithm that determines how nodes share channel, i.e., determine when node can transmit
communication about channel sharing must use channel itself!
  no out-of-band channel for coordination
multiple access protocol

## Slide 19: An ideal multiple access protocol
given: multiple access channel (MAC) of rate R bps
desiderata:
  1. when one node wants to transmit, it can send at rate R.
  2. when M nodes want to transmit, each can send at average rate R/M
  3. fully decentralized:
    no special node to coordinate transmissions
    no synchronization of clocks, slots
  4. simple

## Slide 20: MAC protocols: taxonomy
three broad classes:
channel partitioning
  divide channel into smaller “pieces” (time slots, frequency, code)
  allocate piece to node for exclusive use
random access
  channel not divided, allow collisions
  “recover” from collisions
“taking turns”
  nodes take turns, but nodes with more to send can take longer turns

## Slide 21: Channel partitioning MAC protocols: TDMA
TDMA: time division multiple access
access to channel in “rounds”
each station gets fixed length slot (length = packet transmission time) in each round
unused slots go idle
example: 6-station LAN, 1,3,4 have packets to send, slots 2,5,6 idle
1
3
4
1
3
4
6-slot
frame
6-slot
frame

## Slide 22: Channel partitioning MAC protocols: FDMA
FDMA: frequency division multiple access
channel spectrum divided into frequency bands
each station assigned fixed frequency band
unused transmission time in frequency bands go idle
example: 6-station LAN, 1,3,4 have packet to send, frequency bands 2,5,6 idle
frequency bands
time
FDM cable

## Slide 23: Random access protocols
when node has packet to send
  transmit at full channel data rate R.
  no a priori coordination among nodes
two or more transmitting nodes: “collision”
random access MAC protocol specifies:
  how to detect collisions
  how to recover from collisions (e.g., via delayed retransmissions)
examples of random access MAC protocols:
  ALOHA, slotted ALOHA
  CSMA, CSMA/CD, CSMA/CA

## Slide 24: Slotted ALOHA
assumptions:
all frames same size
time divided into equal size slots (time to transmit 1 frame)
nodes start to transmit only slot beginning
nodes are synchronized
if 2 or more nodes transmit in slot, all nodes detect collision
operation:
when node obtains fresh frame, transmits in next slot
  if no collision: node can send new frame in next slot
  if collision: node retransmits frame in each subsequent slot with probability p until success
randomization – why?

## Slide 25: Slotted ALOHA
Pros:
single active node can continuously transmit at full rate of channel
highly decentralized: only slots in nodes need to be in sync
simple
Cons:
collisions, wasting slots
idle slots
nodes may be able to detect collision in less than time to transmit packet
clock synchronization
1
1
1
1
2
3
2
2
3
3
node 1
node 2
node 3
C
C
C
S
S
S
E
E
E
C: collision
S: success
E: empty

## Slide 26: Pure ALOHA
unslotted Aloha: simpler, no synchronization
  when frame first arrives: transmit immediately
collision probability increases with no synchronization:
  frame sent at t0 collides with other frames sent in [t0-1,t0+1]
t0 + 1
t0 - 1
t0
will overlap
with end of
i’s frame
will overlap
with start of
i’s frame
pure Aloha efficiency: 18% !

## Slide 27: CSMA (carrier sense multiple access)
simple CSMA: listen before transmit:
  if channel sensed idle: transmit entire frame
  if channel sensed busy: defer transmission
human analogy: don’t interrupt others!
CSMA/CD: CSMA with collision detection
  collisions detected within short time
  colliding transmissions aborted, reducing channel wastage
  collision detection easy in wired, difficult with wireless
human analogy: the polite conversationalist

## Slide 28: CSMA: collisions
collisions can still occur with carrier sensing:
  propagation delay means two nodes may not hear each other’s just-started transmission
collision: entire packet transmission time wasted
  distance & propagation delay play role in in determining collision probability
spatial layout of nodes

## Slide 29: CSMA/CD:
CSMA/CS reduces the amount of time wasted in collisions
  transmission aborted on collision detection
spatial layout of nodes

## Slide 30: Ethernet CSMA/CD algorithm
NIC receives datagram from network layer, creates frame
If NIC senses channel:
  if idle: start frame transmission.
  if busy: wait until channel idle, then transmit
If NIC transmits entire frame without collision, NIC is done with frame !
If NIC detects another transmission while sending: abort, send jam signal
After aborting, NIC enters binary (exponential) backoff:
  after mth collision, NIC chooses K at random from {0,1,2, …, 2m-1}. NIC waits K·512 bit times, returns to Step 2
  more collisions: longer backoff interval

## Slide 31: “Taking turns” MAC protocols
channel partitioning MAC protocols:
  share channel efficiently and fairly at high load
  inefficient at low load: delay in channel access, 1/N bandwidth allocated even if only 1 active node!
random access MAC protocols
  efficient at low load: single node can fully utilize channel
  high load: collision overhead
“taking turns” protocols
  look for best of both worlds!

## Slide 32: “Taking turns” MAC protocols
polling:
master node “invites” other nodes to transmit in turn
typically used with “dumb” devices
concerns:
  polling overhead
  latency
  single point of failure (master)
master
slaves
poll
data
data

## Slide 33: “Taking turns” MAC protocols
token passing:
control token passed from one node to next sequentially.
token message
concerns:
  token overhead
  latency
  single point of failure (token)
T
data
(nothing
to send)
T

## Slide 34: Summary of MAC protocols
channel partitioning, by time, frequency or code
  Time Division, Frequency Division
random access (dynamic),
  ALOHA, S-ALOHA, CSMA, CSMA/CD
  carrier sensing: easy in some technologies (wire), hard in others (wireless)
  CSMA/CD used in Ethernet
  CSMA/CA used in 802.11
taking turns
  polling from central site, token passing
  Bluetooth, FDDI, token ring

## Slide 35: Link layer, LANs: roadmap
a day in the life of a web request
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
  VLANs
link virtualization: MPLS
data center networking

## Slide 36: MAC addresses
32-bit IP address:
  network-layer address for interface
  used for layer 3 (network layer) forwarding
  e.g.: 128.119.40.136
MAC (or LAN or physical or Ethernet) address:
  function: used “locally” to get frame from one interface to another physically-connected interface (same subnet, in IP-addressing sense)
  48-bit MAC address (for most LANs) burned in NIC ROM, also sometimes software settable
hexadecimal (base 16) notation
(each “numeral” represents 4 bits)
  e.g.: 1A-2F-BB-76-09-AD

## Slide 37: MAC addresses
each interface on LAN
has unique 48-bit MAC address
has a locally unique 32-bit IP address (as we’ve seen)
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
(wired or wireless)
137.196.7/24
137.196.7.78
137.196.7.14
137.196.7.88
137.196.7.23

## Slide 38: MAC addresses
MAC address allocation administered by IEEE
manufacturer buys portion of MAC address space (to assure uniqueness)
analogy:
  MAC address: like Social Security Number
  IP address: like postal address
MAC flat address: portability
  can move interface from one LAN to another
  recall IP address not portable: depends on IP subnet to which node is attached

## Slide 39: ARP: address resolution protocol
ARP table: each IP node (host, router) on LAN has table
Question: how to determine interface’s MAC address, knowing its IP address?
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
137.196.7.78
137.196.7.14
137.196.7.88
137.196.7.23
ARP
ARP
ARP
ARP
  IP/MAC address mappings for some LAN nodes:
< IP address; MAC address; TTL>
  TTL (Time To Live): time after which address mapping will be forgotten (typically 20 min)

## Slide 40: ARP protocol in action
58-23-D7-FA-20-B0
137.196.7.14
B
C
D
TTL
71-65-F7-2B-08-53
137.196.7.23
A
ARP table in A
IP addr
MAC addr
TTL
example: A wants to send datagram to B
  B’s MAC address not in A’s ARP table, so A uses ARP to find B’s MAC address
A broadcasts ARP query, containing B's IP addr
  destination MAC address = FF-FF-FF-FF-FF-FF
  all nodes on LAN receive ARP query
1
Source MAC: 71-65-F7-2B-08-53
Source IP: 137.196.7.23
Target IP address: 137.196.7.14
…
1
Ethernet frame (sent to FF-FF-FF-FF-FF-FF)

## Slide 41: ARP protocol in action
58-23-D7-FA-20-B0
137.196.7.14
B
C
D
TTL
71-65-F7-2B-08-53
137.196.7.23
A
ARP table in A
IP addr
MAC addr
TTL
example: A wants to send datagram to B
  B’s MAC address not in A’s ARP table, so A uses ARP to find B’s MAC address
B replies to A with ARP response, giving its MAC address
2
Target IP address: 137.196.7.14
Target MAC address:
58-23-D7-FA-20-B0
…
2
ARP message into Ethernet frame (sent to 71-65-F7-2B-08-53)

## Slide 42: ARP protocol in action
58-23-D7-FA-20-B0
137.196.7.14
B
C
D
TTL
71-65-F7-2B-08-53
137.196.7.23
A
ARP table in A
IP addr
MAC addr
TTL
example: A wants to send datagram to B
  B’s MAC address not in A’s ARP table, so A uses ARP to find B’s MAC address
A receives B’s reply, adds B entry into its local ARP table
3
137.196.
7.14
58-23-D7-FA-20-B0
500

## Slide 43: Routing to another subnet: addressing
walkthrough: sending a datagram from A to B via R
  focus on addressing – at IP (datagram) and MAC layer (frame) levels
R
A
B
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
  assume that:
    A knows B’s IP address
    A knows IP address of first hop router, R (how?)
    A knows R’s MAC address (how?)

## Slide 44: Routing to another subnet: addressing
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
IP src: 111.111.111.111
IP dest: 222.222.222.222
A creates IP datagram with IP source A, destination B
A creates link-layer frame containing A-to-B IP datagram
  R's MAC address is frame’s destination
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B

## Slide 45: Routing to another subnet: addressing
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
frame sent from A to R
IP
Eth
Phy
frame received at R, datagram removed, passed up to IP
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B
IP src: 111.111.111.111
IP dest: 222.222.222.222
IP src: 111.111.111.111
IP dest: 222.222.222.222

## Slide 46: Routing to another subnet: addressing
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
R determines outgoing interface, passes datagram with IP source A, destination B to link layer
R creates link-layer frame containing A-to-B IP datagram. Frame destination address: B's MAC address
IP
Eth
Phy

## Slide 47: Routing to another subnet: addressing
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
IP
Eth
Phy
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
transmits link-layer frame
R determines outgoing interface, passes datagram with IP source A, destination B to link layer
R creates link-layer frame containing A-to-B IP datagram. Frame destination address: B's MAC address

## Slide 48: Routing to another subnet: addressing
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
IP
Eth
Phy
B receives frame, extracts IP datagram destination B
B passes datagram up protocol stack to IP
IP src: 111.111.111.111
IP dest: 222.222.222.222

## Slide 49: Link layer, LANs: roadmap
a day in the life of a web request
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
  VLANs
link virtualization: MPLS
data center networking

## Slide 50: Ethernet
“dominant” wired LAN technology:
first widely used LAN technology
simpler, cheap
kept up with speed race: 10 Mbps – 400 Gbps
single chip, multiple speeds (e.g., Broadcom BCM5761)
Metcalfe’s Ethernet sketch
https://www.uspto.gov/learning-and-resources/journeys-innovation/audio-stories/defying-doubters

## Slide 51: Ethernet: physical topology
bus: popular through mid 90s
  all nodes in same collision domain (can collide with each other)
bus: coaxial cable
switched
switched: prevails today
  active link-layer 2 switch in center
  each “spoke” runs a (separate) Ethernet protocol (nodes do not collide with each other)

## Slide 52: Ethernet frame structure
sending interface encapsulates IP datagram (or other network layer protocol packet) in Ethernet frame
dest.
address
source
address
data (payload)
CRC
preamble
type
preamble:
used to synchronize receiver, sender clock rates
7 bytes of 10101010 followed by one byte of 10101011

## Slide 53: Ethernet frame structure (more)
dest.
address
source
address
data (payload)
CRC
preamble
type
addresses: 6 byte source, destination MAC addresses
  if adapter receives frame with matching destination address, or with broadcast address (e.g., ARP packet), it passes data in frame to network layer protocol
  otherwise, adapter discards frame
type: indicates higher layer protocol
  mostly IP but others possible, e.g., Novell IPX, AppleTalk
  used to demultiplex up at receiver
CRC: cyclic redundancy check at receiver
  error detected: frame is dropped

## Slide 54: Ethernet: unreliable, connectionless
connectionless: no handshaking between sending and receiving NICs
unreliable: receiving NIC doesn’t send ACKs or NAKs to sending NIC
  data in dropped frames recovered only if initial sender uses higher layer rdt (e.g., TCP), otherwise dropped data lost
Ethernet’s MAC protocol: unslotted CSMA/CD with binary backoff

## Slide 55: 802.3 Ethernet standards: link & physical layers
  different physical layer media: fiber, cable
application
transport
network
link
physical
MAC protocol
and frame format
100BASE-TX
100BASE-T4
100BASE-FX
100BASE-T2
100BASE-SX
100BASE-BX
fiber physical layer
copper (twister pair) physical layer
many different Ethernet standards
  common MAC protocol and frame format
  different speeds: 2 Mbps, 10 Mbps, 100 Mbps, 1Gbps, 10 Gbps, 40 Gbps

## Slide 56: Link layer, LANs: roadmap
a day in the life of a web request
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
  VLANs
link virtualization: MPLS
data center networking

## Slide 57: Ethernet switch
Switch is a link-layer device: takes an active role
  store, forward Ethernet frames
  examine incoming frame’s MAC address, selectively forward frame to one-or-more outgoing links when frame is to be forwarded on segment, uses CSMA/CD to access segment
transparent: hosts unaware of presence of switches
plug-and-play, self-learning
  switches do not need to be configured

## Slide 58: Switch: multiple simultaneous transmissions
switch with six interfaces (1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6
hosts have dedicated, direct connection to switch
switches buffer packets
Ethernet protocol used on each incoming link, so:
  no collisions; full duplex
  each link is its own collision domain
switching: A-to-A’ and B-to-B’ can transmit simultaneously, without collisions

## Slide 59: Switch: multiple simultaneous transmissions
switch with six interfaces (1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6
hosts have dedicated, direct connection to switch
switches buffer packets
Ethernet protocol used on each incoming link, so:
  no collisions; full duplex
  each link is its own collision domain
switching: A-to-A’ and B-to-B’ can transmit simultaneously, without collisions
  but A-to-A’ and C to A’ can not happen simultaneously

## Slide 60: Switch forwarding table
A
A’
B
B’
C
C’
1
2
3
4
5
6
Q: how does switch know A’ reachable via interface 4, B’ reachable via interface 5?
A: each switch has a switch table, each entry:
  (MAC address of host, interface to reach host, time stamp)
  looks like a routing table!
Q: how are entries created, maintained in switch table?
  something like a routing protocol?

## Slide 61: Switch: self-learning
A
A’
B
B’
C
C’
1
2
3
4
5
6
switch learns which hosts can be reached through which interfaces
A A’
Source: A
Dest: A’
MAC addr interface TTL
Switch table
(initially empty)
A
1
60
  when frame received, switch “learns” location of sender: incoming LAN segment
  records sender/location pair in switch table

## Slide 62: Switch: frame filtering/forwarding
when frame received at switch:
  1. record incoming link, MAC address of sending host
  2. index switch table using MAC destination address
  3. if entry found for destination then {
  if destination on segment from which frame arrived then drop frame
  else forward frame on interface indicated by entry
  }
  else flood /* forward on all interfaces except arriving interface */

## Slide 63: Self-learning, forwarding: example
A
A’
B
B’
C
C’
1
2
3
4
5
6
A A’
Source: A
Dest: A’
MAC addr interface TTL
switch table
(initially empty)
A
1
60
A A’
A A’
A A’
A A’
A A’
A’ A
A’
4
60
frame destination, A’, location unknown:
flood
destination A location known:
selectively send
on just one link

## Slide 64: Interconnecting switches
self-learning switches can be connected together:
Q: sending from A to G - how does S1 know to forward frame destined to G via S4 and S3?
A: self learning! (works exactly the same as in single-switch case!)
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G

## Slide 65: Self-learning multi-switch example
Suppose C sends frame to I, I responds to C
Q: show switch tables and packet forwarding in S1, S2, S3, S4
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G

## Slide 66: Small institutional network
to external
network
router
IP subnet
mail server
web server

## Slide 67: Switches vs. routers
application
transport
network
link
physical
network
link
physical
link
physical
switch
datagram
application
transport
network
link
physical
frame
frame
frame
datagram
6-67
both are store-and-forward:
routers: network-layer devices (examine network-layer headers)
switches: link-layer devices (examine link-layer headers)
both have forwarding tables:
routers: compute tables using routing algorithms, IP addresses
switches: learn forwarding table using flooding, learning, MAC addresses

## Slide 68: Link layer, LANs: roadmap
a day in the life of a web request
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches

## Slide 69: Link layer, LANs: roadmap
a day in the life of a web request
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches

## Slide 70: Synthesis: a day in the life of a web request
our journey down the protocol stack is now complete!
  application, transport, network, link
putting-it-all-together: synthesis!
  goal: identify, review, understand protocols (at all layers) involved in seemingly simple scenario: requesting www page
  scenario: student attaches laptop to campus network, requests/receives www.google.com

## Slide 71: A day in the life: scenario
Comcast network
68.80.0.0/13
Google’s network
64.233.160.0/19
64.233.169.105
web server
DNS server
school network
68.80.2.0/24
browser
web page
arriving mobile client attaches to network …
requests web page: www.google.com
scenario:
Sounds
simple!

## Slide 72: A day in the life: connecting to the Internet
router has
DHCP server
arriving mobile:
DHCP client
connecting laptop needs to get its own IP address, addr of first-hop router, addr of DNS server: use DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.3 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP

## Slide 73: A day in the life: connecting to the Internet
router has
DHCP server
arriving mobile:
DHCP client
DHCP
UDP
IP
Eth
Phy
DHCP
UDP
IP
Eth
Phy
DHCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
encapsulation at DHCP server, frame forwarded (switch learning) through LAN, demultiplexing at client
Client now has IP address, knows name & addr of DNS
server, IP address of its first-hop router
DHCP client receives DHCP ACK reply

## Slide 74: A day in the life… ARP (before DNS, before HTTP)
router has
ARP server
arriving mobile:
ARP client
DNS
UDP
IP
Eth
Phy
Eth
Phy
ARP
before sending HTTP request, need IP address of www.google.com: DNS
DNS
DNS
DNS
DNS query created, encapsulated in UDP, encapsulated in IP, encapsulated in Eth. To send frame to router, need MAC address of router interface: ARP
ARP query broadcast, received by router, which replies with ARP reply giving MAC address of router interface
client now knows MAC address of first hop router, so can now send frame containing DNS query
ARP query
ARP
ARP reply

## Slide 75: A day in the life… using DNS
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
Comcast network
68.80.0.0/13
DNS
server
DNS
DNS
DNS
DNS
DNS
IP datagram containing DNS query forwarded via LAN switch from client to 1st hop router
IP datagram forwarded from campus network into Comcast network, routed (tables created by RIP, OSPF, IS-IS and/or BGP routing protocols) to DNS server
demuxed to DNS
DNS replies to client with IP address of www.google.com
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS
DNS

## Slide 76: A day in the life…TCP connection carrying HTTP
DNS
DNS
DNS
Comcast network
68.80.0.0/13
64.233.169.105
Google web server
HTTP
TCP
IP
Eth
Phy
HTTP
to send HTTP request, client first opens TCP socket to web server
TCP SYN segment (step 1 in TCP 3-way handshake) inter-domain routed to web server
TCP connection established!
SYN
SYN
SYN
SYN
TCP
IP
Eth
Phy
SYN
SYN
SYN
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
web server responds with TCP SYNACK (step 2 in TCP 3-way handshake)

## Slide 77: A day in the life… HTTP request/reply
DNS
DNS
DNS
Comcast network
68.80.0.0/13
64.233.169.105
Google web server
HTTP
TCP
IP
Eth
Phy
HTTP
TCP
IP
Eth
Phy
HTTP
HTTP request sent into TCP socket
IP datagram containing HTTP request routed to www.google.com
IP datagram containing HTTP reply routed back to client
web server responds with HTTP reply (containing web page)
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
web page finally (!!!) displayed

## Slide 78: Chapter 6: Summary
principles behind data link layer services:
  error detection, correction
  sharing a broadcast channel: multiple access
  link layer addressing
instantiation, implementation of various link layer technologies
  Ethernet
  switched LANS
synthesis: a day in the life of a web request

## Slide 79: Chapter 6: let’s take a breath
journey down protocol stack complete (except PHY)
solid understanding of networking principles, practice!
….. could stop here …. but more interesting topics!
  wireless
  security

## Slide 80: Additional Chapter 6 slides

## Slide 81: Pure ALOHA efficiency
P(success by given node) = P(node transmits)
P(no other node transmits in [t0-1,t0]
P(no other node transmits in [t0-1,t0]
= p . (1-p)N-1 . (1-p)N-1
= p . (1-p)2(N-1)
… choosing optimum p and then letting n
= 1/(2e) = .18
*
*
*
even worse than slotted Aloha!