## Slide 1: Physical Layer
McGraw-Hill
©The McGraw-Hill Companies, Inc., 2000
1

## Slide 2: Chapter 3
Introduction To
Physical Layer
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.

## Slide 3: Chapter 3: Outline
  DATA AND SIGNALS
  PERIODIC ANALOG SIGNALS
  DIGITAL SIGNALS
  TRANSMISSION IMPAIRMENT
  DATA RATE LIMITS
  PERFORMANCE

## Slide 4: 3.1.1 Analog and Digital Data
Data can be analog or digital. The term analog data refers to information that is continuous; digital data refers to information that has discrete states. For example, an analog clock that has hour, minute, and second hands gives information in a continuous form; the movements of the hands are continuous. On the other hand, a digital clock that reports the hours and the minutes will change suddenly from 8:05 to 8:06.

## Slide 5: Figure 3.2: Comparison of analog and digital signals

## Slide 6: 3.1.3 Periodic and Nonperiodic
A periodic signal completes a pattern within a measurable time frame, called a period, and repeats that pattern over subsequent identical periods. The completion of one full pattern is called a cycle. A nonperiodic signal changes without exhibiting a pattern or cycle that repeats over time.

## Slide 7: 3.2.1 Sine Wave
The sine wave is the most fundamental form of a periodic analog signal. When we visualize it as a simple oscillating curve, its change over the course of a cycle is smooth and consistent, a continuous, rolling flow. Figure 3.3 shows a sine wave. Each cycle consists of a single arc above the time axis followed by a single arc below it.

## Slide 8: Figure 3.3: A sine wave
• • •
Time
Value

## Slide 9: Figure 3.4: Two signals with two different amplitudes
Peak amplitude
Peak amplitude

## Slide 10: Figure 3.5: Two signals with same phase, different amplitudes and frequency

## Slide 11: Table 3.1: Units of period and frequency

## Slide 12: Example 3.4
Express a period of 100 ms in microseconds.
Solution
From Table 3.1 we find the equivalents of 1 ms (1 ms is 10–
3 s) and 1 s (1 s is 106 μs). We make the following substitutions:

## Slide 13: Example 3.3
The power we use at home has a frequency of 60 Hz (50 Hz in Europe). The period of this sine wave can be determined as follows:
This means that the period of the power for our lights at home is 0.0116 s, or 16.6 ms. Our eyes are not sensitive enough to distinguish these rapid changes in amplitude.

## Slide 14: Example 3.5
The period of a signal is 100 ms. What is its frequency in kilohertz?.
Solution
First we change 100 ms to seconds, and then we calculate the frequency from the period (1 Hz = 10–3 kHz).

## Slide 15: 3.2.3 Wavelength
Wavelength is another characteristic of a signal traveling through a transmission medium. Wavelength binds the period or the frequency of a simple sine wave to the propagation speed of the medium (see Figure 3.7).

## Slide 16
Figure 3.7: Wavelength and period
Wavelength
Direction of propagation

## Slide 17: Example 3.8
Figure 3.10 shows a periodic composite signal with frequency f. This type of signal is not typical of those found in data communications. We can consider it to be three alarm systems, each with a different frequency. The analysis of this signal can give us a good understanding of how to decompose signals. It is very difficult to manually decompose this signal into a series of simple sine waves.
However, there are tools, both hardware and software, that can help us do the job. We are not concerned
about how it is done; we are only interested in the result. Figure 3.11 shows the result of decomposing the above signal in both the time and frequency domains.

## Slide 18: Figure 3.10: A composite periodic signal

## Slide 19: Figure 3.11: Decomposition of a composite periodic signal
• • •
Time
Amplitude
Amplitude
f
3f 9f
b. Frequency-domain decomposition of the composite signal
Frequency

## Slide 20: Example 3.9
Figure 3.12 shows a nonperiodic composite signal. It can be the signal created by a microphone or a telephone set when a word or two is pronounced. In this case, the composite signal cannot be periodic, because that implies that we are repeating the same word or words with exactly the
same tone.

## Slide 21: Figure 3.12: Time and frequency domain of a non-periodic signal

## Slide 22: 3.2.6 Bandwidth
The range of frequencies contained in a composite signal is its bandwidth. The bandwidth is normally a difference between two numbers. For example, if a composite signal contains frequencies between 1000 and 5000, its bandwidth is 5000 − 1000, or 4000.

## Slide 23: Figure 3.13: The bandwidth of periodic and nonperiodic composite signals

## Slide 24: Example 3.10
If a periodic signal is decomposed into five sine waves with frequencies of 100, 300, 500, 700, and 900 Hz, what is its bandwidth? Draw the spectrum, assuming all components have a maximum amplitude of 10 V.
Solution
Let fh be the highest frequency, fl the lowest frequency, and B the bandwidth. Then

## Slide 25: Figure 3.14: The bandwidth for example 3.10

## Slide 26: Example 3.11
A periodic signal has a bandwidth of 20 Hz. The highest frequency is 60 Hz. What is the lowest frequency? Draw the spectrum if the signal contains all frequencies of the same amplitude.
Solution
Let fh be the highest frequency, fl the lowest frequency, and B the bandwidth. Then
The spectrum contains all integer frequencies. We show this by a series of spikes (see Figure 3.15).

## Slide 27: Figure 3.15: The bandwidth for example 3.11

## Slide 28: 3-3 DIGITAL SIGNALS
In addition to being represented by an analog signal, information can also be represented by a digital signal. For example, a 1 can be encoded as a positive voltage and a 0 as zero voltage. A digital signal can have more than two levels. In this case, we can send more than 1 bit for each level. Figure
3.17 shows two signals, one with two levels and the other with four.

## Slide 29: Figure 3.17: Two digital signals: one with two signal levels and the other with four signal levels

## Slide 30: Example 3.16
A digital signal has eight levels. How many bits are needed per level? We calculate the number of bits from the following formula. Each signal level is represented by 3 bits.

## Slide 31: Example 3.17
A digital signal has nine levels. How many bits are needed per level? We calculate the number of bits by using the formula. Each signal level is represented by 3.17 bits. However, this answer is not realistic. The number of bits sent per level needs to be an integer as well as a power of 2. For this example, 4 bits can represent one level.

## Slide 32: 3.3.1 Bit Rate
Most digital signals are nonperiodic, and thus period and frequency are not appropriate characteristics. Another term—bit rate (instead of frequency)—is used to describe digital signals. The bit rate is the number of bits sent in 1s, expressed in bits per second (bps). Figure 3.17 shows the bit rate for two signals.

## Slide 33: Example 3.18
Assume we need to download text documents at the rate of 100 pages per second. What is the required bit rate of the channel? A page is an average of 24 lines with 80 characters in each line.
Solution
From Table 3.1 we find the equivalents of 1 ms (1 ms is 10–
3 s) and 1 s (1 s is 106 μs). We make the following substitutions:

## Slide 34: 3-4 TRANSMISSION IMPAIRMENT
Signals travel through transmission media, which are not perfect. The imperfection causes signal impairment. This means that the signal at the beginning of the medium is not the same as the signal at the end of the medium. What is sent is not what is received.
Three causes of impairment are attenuation,
distortion, and
noise (see Figure 3.26).

## Slide 35: Figure 3.26: Causes of impairment

## Slide 36: 3.4.1 Attenuation
Attenuation means a loss of energy. When a signal, simple or composite, travels through a medium, it loses some of its energy in overcoming the resistance of the medium. That is why a wire carrying electric signals gets warm, if not hot, after a while. Some of the electrical energy in the signal is converted to heat. To compensate for this loss, amplifiers are used to amplify the signal. Figure 3.27 shows the effect of attenuation and amplification..

## Slide 37: Figure 3.27: Attenuation and amplification

## Slide 38: Example 3.26
Suppose a signal travels through a transmission medium and its power is reduced to one half. This means that P2 = 0.5 P1. In this case, the attenuation (loss of power) can be calculated as
A loss of 3 dB (−3 dB) is equivalent to losing one-half the power.

## Slide 39
A signal travels through an amplifier, and its power is increased 10 times. This means that P2 = 10P1. In this case, the amplification (gain of power) can be calculated as
Example 3.27

## Slide 43: 3.4.2 Distortion
Distortion means that the signal changes its form or shape. Distortion can occur in a composite signal made of different frequencies. Each signal component has its own propagation speed (see the next section) through a medium and, therefore, its own delay in arriving at the final destination. Differences in delay may create a difference in phase if the delay is not exactly the same as the period duration.

## Slide 44: Figure 3.29: Distortion

## Slide 45: 3.4.3 Noise
Noise is another cause of impairment. Several types of noise, such as thermal noise, induced noise, crosstalk, and impulse noise, may corrupt the signal. Thermal noise is the random motion of electrons in a wire, which creates an extra signal not originally sent by the transmitter. Induced noise comes from sources such as motors. Crosstalk is the effect of one wire on the other.

## Slide 46: Figure 3.30: Noise

## Slide 47: Figure 3.31: Two cases of SNR: a high SNR and a low SNR

## Slide 48: Example 3.31
The power of a signal is 10 mW and the power of the noise is 1 μW; what are the values of SNR and SNRdB?
Solution
The values of SNR and SNRdB can be calculated as follows:

## Slide 49: Example 3.32
The values of SNR and SNRdB for a noiseless channel are
Solution
The values of SNR and SNRdB for a noiseless channel are
We can never achieve this ratio in real life; it is an ideal.

## Slide 50: 3-5 DATA RATE LIMITS
A very
important consideration in data
communications is how fast we can send data,
in bits per theoretical
second, over a formulas were
channel. Two developed to
calculate the data rate: one by Nyquist for a noiseless channel, another by Shannon for a noisy channel.

## Slide 51: 3.5.1 Noiseless Channel: Nyquist Rate
For a noiseless channel, the Nyquist bit rate formula defines the theoretical maximum bit rate.

## Slide 52
Consider a noiseless channel with a bandwidth of 3000 Hz transmitting a signal with two signal levels. The maximum bit rate can be calculated as
Example 3.34

## Slide 53
Consider the same noiseless channel transmitting a signal with four signal levels (for each level, we send 2 bits). The maximum bit rate can be calculated as
Example 3.35

## Slide 54: Example 3.36
We need to send 265 kbps over a noiseless channel with a bandwidth of 20 kHz. How many signal levels do we need?
Solution
We can use the Nyquist formula as shown:
Since this result is not a power of 2, we need to either increase the number of levels or reduce the bit rate. If we have 128 levels, the bit rate is 280 kbps. If we have 64 levels, the bit rate is 240 kbps.

## Slide 55: 3.5.2 Noisy Channel: Shannon Capacity
In reality, we cannot have a noiseless channel; the channel is always noisy. In 1944, Claude Shannon introduced a formula, called the Shannon capacity, to determine the theoretical highest data rate for a noisy channel:

## Slide 56: Example 3.37
Consider an extremely noisy channel in which the value of the signal-to-noise ratio is almost zero. In other words, the noise is so strong that the signal is faint. For this channel the capacity C is calculated as
This means that the capacity of this channel is zero regardless of the bandwidth. In other
words, we cannot receive any data through this channel.

## Slide 57
The signal-to-noise ratio is often given in decibels. Assume that SNRdB = 36 and the channel bandwidth is 2 MHz. The theoretical channel capacity can be calculated as
Example 3.39

## Slide 58
3.5.3 Using Both Limits
In practice, we need to use both methods to find the limits and signal levels. Let us show this with an example.

## Slide 59: Example 3.41
We have a channel with a 1-MHz bandwidth. The SNR for this channel is 63. What are the appropriate bit rate and signal level?
Solution
First, we use the Shannon formula to find the upper limit.
The Shannon formula gives us 6 Mbps, the upper limit. For better performance we choose something lower, 4 Mbps. Then we use the Nyquist formula to find the number of signal levels.

## Slide 60: 3.6.1 Bandwidth
One characteristic that measures network performance is bandwidth. However, the term can be used in two different contexts with two different measuring values: bandwidth in hertz and bandwidth in bits per second..

## Slide 61: Example 3.42
The bandwidth of a subscriber line is 4 kHz for voice or data. The bandwidth of this line for data transmission
can be up to 56,000 bps using a sophisticated modem to change the digital signal to analog.

## Slide 62: Example 3.43
If the telephone company improves the quality of the line and increases the bandwidth to 8 kHz, we can send 112,000 bps by using the same technology as mentioned in Example 3.42.

## Slide 63: 3.6.2 Throughput
The throughput is a measure of how fast we can actually send data through a network. Although, at first glance, bandwidth in bits per second and throughput seem the same, they are different. A link may have a bandwidth of B bps, but we can only send T bps through this link with T always less than B.

## Slide 64: 3.6.3 Throughput
The latency or delay defines how long it takes for an entire message to completely arrive at the destination from the time the first bit is sent out from the source. We can say that latency is made of four components: propagation time, transmission time, queuing time and processing delay.

## Slide 65: Example 3.44
A network with bandwidth of 10 Mbps can pass only an average of 12,000 frames per minute with each frame carrying an average of 10,000 bits. What is the throughput of this network?
Solution
We can calculate the throughput as
The throughput is almost one-fifth of the bandwidth in this case.

## Slide 66: Example 3.45
What is the propagation time if the distance between the two points is 12,000 km? Assume the propagation speed to be
2.4 × 108 m/s in cable.
Solution
We can calculate the propagation time as
The example shows that a bit can go over the Atlantic Ocean in only 50 ms if there is a direct cable between the source and the destination.

## Slide 67: Example 3.46
What are the propagation time and the transmission time for a 2.5-KB (kilobyte) message if the bandwidth of the network is 1 Gbps? Assume that the distance between the sender and the receiver is 12,000 km and that light travels at 2.4 × 108 m/s.
Solution
We can calculate the propagation and transmission time as
Note that in this case, because the message is short and the bandwidth is high, the dominant factor is the propagation time, not the transmission time.

## Slide 68: Example 3.47
What are the propagation time and the transmission time for a 5-MB (megabyte) message (an image) if the bandwidth of the network is 1 Mbps? Assume that the distance between the sender and the receiver is 12,000 km and that light travels at 2.4 × 108 m/s.
Solution
We can calculate the propagation and transmission times as
We can calculate the propagation and transmission times as